## Slide 1: Schedulability analysis of limited-preemptive moldable gang tasks
3rd of June, 2020
Geoffrey Nelissen
Mitra Nasri
Joan Marcè i Igual
Daily Supervisor
Co-supervisor

## Slide 2: Real-time systems
Systems of which correctness does depends not only on logical results but also on timing constraints
Multicore systems

## Slide 3: Definitions
Task
  A functionality of the system
Job
  Instance of a task
Schedule
  A particular assignment of jobs to the processors and time intervals
Scheduling policy
  Algorithm that produces a schedule
  FIFO, Round-Robin, JLFP, EDF
Notes: Example task: Task that controls

## Slide 4: What is gang?
Parallel threads together as a “gang”
Execution does not start until there are enough cores
Global scheduling
Gang Scheduling
IDLE

## Slide 5: Why gang?
More efficient synchronization
Reduces variability in the execution
Avoids overhead when loading initial data
Shows its full potential when executed non-preemptively
Global scheduling
Gang Scheduling
Notes: Global scheduling would load the same data multiple times
Gang scheduling would load the data once for all the jobs
This is more evident in non-preemptive execution

## Slide 6: Types of gang
Rigid: number of cores set by programmer
Moldable: number of cores assigned when job is dispatched
Malleable: number of cores can change during runtime
👎Wastes resources
👎Hard to implement
👍Flexibility
Notes: Three types:
Rigid gang: Number of cores fixed by programmer
Moldable gang: Number of cores between minimum and maximum. Scheduler chooses at scheduling time.
Malleable gang: Number of cores between minimum and maximum. Can vary during runtime
We choose moldable because:
Rigid can incur in loss of performance if not all cores are actually used
Malleable is hard to implement in reality

## Slide 7: Bundled scheduling[1] vs limited-preemptive
[1]Wasly et al., 2017
Notes: Example, three bundles.

## Slide 8: Bundled scheduling[1] vs limited-preemptive
Rigid gang reserves the whole block
Bundled creates rigid blocks with dependencies
Limited-Preemptive creates moldable blocks with dependencies
Rigid gang scheduling
Bundled model scheduling
Limited-Preemptive scheduling
WASTED
[1]Wasly et al., 2017
WASTED
Notes: Rigid gang reserves a whole block for the three bundles
Bundled scheduling creates three individual rigid bundles
Limited-Preemptive creates three individual moldable bundles

## Slide 9: Job-level fixed-priority scheduling (JLFP) for gang
Based on global JLFP scheduler
Assigns maximum number of available cores to a job between the range of cores that the job allows
Scheduling:
Scheduling:
JLFP scheduler
 | Priority | Min cores | Max cores | Deadline | Execution time
 | High | 2 | 3 |  | 15, 10
 | Low | 2 | 2 | 20 | 15
 | Priority | Min cores | Max cores | Deadline | Execution time
 | High | 2 | 3 |  | 15, 10
 | Low | 2 | 2 | 20 | 15
 | Priority | Min cores | Max cores | Deadline | Execution time
 | High | 2 | 3 |  | 15, 10
 | Low | 2 | 2 | 20 | 15
 | Priority | Min cores | Max cores | Deadline | Execution time
 | High | 2 | 3 |  | 15, 10
 | Low | 2 | 2 | 20 | 15
 | Priority | Min cores | Max cores | Deadline | Execution time
 | High | 2 | 3 |  | 15, 10
 | Low | 2 | 2 | 20 | 15
 | Priority | Min cores | Max cores | Deadline | Execution time
 | High | 2 | 3 |  | 15, 10
 | Low | 2 | 2 | 20 | 15

## Slide 10: Previous work
[1]Ousterhout, 1982
[2]Goossens et al., 2010
[4]Goossens et al., 2016
[5]Berten et al., 2011
Introduced in high-performance computing in 1982[1]
[3]Kato et al., 2009
Preemptive solutions
Schedulers
Schedulability tests
Non-preemptive solutions
Job-level fixed-priority[2]
Earliest deadline first[3]
Optimal for rigid gang (DP-Fair)[4]
Moldable gang[5]
Schedulability tests
Earliest deadline first for rigid gang[6]
[6]Dong et al. 2019
Notes: Introduced in high-performance computing
Real-time:
  Fixed-priority is not predictable
  Fully-preemptive solutions:
    Optimal scheduler for rigid gang but high number of preemptions
    Moldable scheduler using moldable property to match deadlines
  Bundled scheduling:
    Precedence constraints modelled as a succession of bundles
    LP definition comes from here
What are the problems that we want to solve?
  Gang scheduling works best in non-preemptive solutions but no-one else has worked on that
  Rigid and moldable models have overhead when using precedence constraints
  There are no good moldable schedulers

## Slide 11: Our work

## Slide 12: Project goals
Design an accurate schedulability analysis for limited-preemptive moldable gang tasks
Evaluate the impact of the level of parallelism assigned to the jobs
Propose a new scheduling algorithm to improve the schedulability of limited-preemptive moldable gang tasks

## Slide 13: Agenda
Gang schedulability analysis
New scheduling policy

## Slide 14: Schedule abstraction graph
It is a technique that allows:
  Search for all possible schedules
  Aggregate “similar” schedules
Every edge is a different scheduler decision
Every node is a different system state

## Slide 15: SAG analysis changes for gang
Previously a state was created for every schedulable job
Now a state is created for every job and possible number of cores
Can stimulate state-space explosion

## Slide 16: SAG analysis changes for gang
Purge states by checking that
  cores available
  More cores not available
  Precedence constraints are respected
Exploring more states
  👍 Is safe, does not make analysis invalid
  👎 Slower and more pessimistic
Proofs
Initial state empty

## Slide 17: Our analysis results
Randomly generated task sets
System processors: 8
System tasks: 20 rigid tasks
Execution time variation: 50%
SCHEDULABLE
UNKNOWN
This project (sufficient test)
State-of-the-art
(sufficient test)
This project (sufficient test)

## Slide 18: Our analysis results
Randomly generated task sets
System processors: 8
System tasks: 20 moldable tasks
Execution time variation: 50%

## Slide 19: Agenda
Gang schedulability analysis
New scheduling policy

## Slide 20: JLFP limitations with moldable gang
Limited-Preemptive Moldable Reservation Gang Scheduler
Non-work conserving scheduler
Reserve cores of higher-priority tasks and distribute the remaining ones among lower priority tasks
Scheduling:
Scheduling:
Scheduling:
Scheduling:
JLFP scheduler
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20

## Slide 21: Reservation-based gang scheduler
Reservation-based
Reserve cores of higher-priority tasks and distribute the remaining ones among lower priority tasks
Non-work conserving scheduler
Scheduling:
Scheduling:
Scheduling:
Scheduling:
ResG scheduler
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20

## Slide 22: Results JLFP vs ResG in simulator
This work
Baseline (JLFP)
System utilization %
Schedulability %
64%
55%
33%
Evaluated in simulator
Randomly generated task sets

## Slide 23: Conclusions
With a better scheduling policy one can improve the schedulability of moldable gang tasks

## Slide 24: Summary
A new analysis for gang tasks using SAG has been defined
A new scheduling policy that uses gang moldable properties has been created

## Slide 25: Next steps
Further reduce sources of pessimism
Provide analysis for ResG scheduler and respective proofs
Thorough evaluation of results using SURFSara cluster
Notes: CLUSTER:
Higher confidence in the results
Test more parameters
Evaluate more systems

## Slide 26: Questions?

## Slide 27: How does SAG work?
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
Notes: Example of graph exploration:
If goes first no deadline miss
If goes first then has a deadline miss later
Example of graph exploration:
If 𝐽_1 goes first no deadline miss
If 𝐽_2 goes first then 𝐽_1 has a deadline miss later

## Slide 28: SAG analysis changes for gang
Check if execution with cores is possible
cores available
cores not available

## Slide 29: Colours
Primary
Boxes
Emphasis
Borders
Notes: SAG is the bridge between tests and simulations
Accurate and relatively fast
Explore space of possible schedules
Model scheduler decisions