## Slide 1: Schedulability analysis of limited-preemptive moldable gang tasks
27th of August, 2020
Geoffrey Nelissen
Mitra Nasri
Joan Marcè i Igual
Daily Supervisor
Co-supervisor

## Slide 2: Real-time systems
Systems of which correctness does depends not only on logical results but also on timing constraints
Multicore systems

## Slide 3: Definitions
Task
  A functionality of the system
Job
  Instance of a task
Schedule
  A particular assignment of jobs to the processors and time intervals
Scheduling policy
  Algorithm that produces a schedule
  FIFO, Round-Robin, JLFP, EDF
Notes: Example task: Task that controls

## Slide 4: What is gang?
Parallel threads together as a “gang”
Execution does not start until there are enough cores
Global scheduling
Gang Scheduling
IDLE

## Slide 5: Why gang?
More efficient synchronization
Reduces variability in the execution
Avoids overhead when loading initial data
Shows its full potential when executed non-preemptively
Global scheduling
Gang Scheduling
Notes: Global scheduling would load the same data multiple times
Gang scheduling would load the data once for all the jobs
This is more evident in non-preemptive execution

## Slide 6: Types of gang
Rigid: number of cores set by programmer
Moldable: number of cores assigned when job is dispatched
Malleable: number of cores can change during runtime
👎Wastes resources
👎Hard to implement
👍Flexibility
Notes: Three types:
Rigid gang: Number of cores fixed by programmer
Moldable gang: Number of cores between minimum and maximum. Scheduler chooses at scheduling time.
Malleable gang: Number of cores between minimum and maximum. Can vary during runtime
We choose moldable because:
Rigid can incur in loss of performance if not all cores are actually used
Malleable is hard to implement in reality

## Slide 7: Bundled scheduling[1] vs limited-preemptive
[1]Wasly et al., 2017
Notes: Example, three bundles.

## Slide 8: Bundled scheduling[1] vs limited-preemptive
Rigid gang reserves the whole block
Bundled creates rigid blocks with dependencies
Limited-Preemptive creates moldable blocks with dependencies
Rigid gang scheduling
Bundled model scheduling
Limited-Preemptive scheduling
WASTED
[1]Wasly et al., 2017
WASTED
Notes: Rigid gang reserves a whole block for the three bundles
Bundled scheduling creates three individual rigid bundles
Limited-Preemptive creates three individual moldable bundles

## Slide 9: Job-level fixed-priority scheduling (JLFP) for gang
Based on global JLFP scheduler
Assigns maximum number of available cores to a job between the range of cores that the job allows
Scheduling:
Scheduling:
JLFP scheduler
 | Priority | Min cores | Max cores | Deadline | Execution time
 | High | 2 | 3 |  | 15, 10
 | Low | 2 | 2 | 20 | 15
 | Priority | Min cores | Max cores | Deadline | Execution time
 | High | 2 | 3 |  | 15, 10
 | Low | 2 | 2 | 20 | 15
 | Priority | Min cores | Max cores | Deadline | Execution time
 | High | 2 | 3 |  | 15, 10
 | Low | 2 | 2 | 20 | 15
 | Priority | Min cores | Max cores | Deadline | Execution time
 | High | 2 | 3 |  | 15, 10
 | Low | 2 | 2 | 20 | 15
 | Priority | Min cores | Max cores | Deadline | Execution time
 | High | 2 | 3 |  | 15, 10
 | Low | 2 | 2 | 20 | 15
 | Priority | Min cores | Max cores | Deadline | Execution time
 | High | 2 | 3 |  | 15, 10
 | Low | 2 | 2 | 20 | 15

## Slide 10: Previous work
[1]Ousterhout, 1982
[2]Goossens et al., 2010
[4]Goossens et al., 2016
[5]Berten et al., 2011
Introduced in high-performance computing in 1982[1]
[3]Kato et al., 2009
Preemptive solutions
Schedulers
Schedulability tests
Non-preemptive solutions
Job-level fixed-priority[2]
Earliest deadline first[3]
Optimal for rigid gang (DP-Fair)[4]
Moldable gang[5]
Schedulability tests
Earliest deadline first for rigid gang[6]
[6]Dong et al. 2019
Notes: Introduced in high-performance computing
Real-time:
  Fixed-priority is not predictable
  Fully-preemptive solutions:
    Optimal scheduler for rigid gang but high number of preemptions
    Moldable scheduler using moldable property to match deadlines
  Bundled scheduling:
    Precedence constraints modelled as a succession of bundles
    LP definition comes from here
What are the problems that we want to solve?
  Gang scheduling works best in non-preemptive solutions but no-one else has worked on that
  Rigid and moldable models have overhead when using precedence constraints
  There are no good moldable schedulers

## Slide 11: Our work

## Slide 12: Project goals
Design an accurate schedulability analysis for limited-preemptive moldable gang tasks
Evaluate the impact of the level of parallelism assigned to the jobs
Propose a new scheduling algorithm to improve the schedulability of limited-preemptive moldable gang tasks

## Slide 13: Agenda
Gang schedulability analysis
New scheduling policy

## Slide 14: Schedule abstraction graph
It is a technique that allows:
  Search for all possible schedules
  Aggregate “similar” schedules
Every edge is a different scheduler decision
Every node is a different system state

## Slide 15: Extending SAG
Update system state representation
Update expansion rules
Update merge rules

## Slide 16: New state representation
We already had core availabilities
We need to keep track of
  Groups of cores
  Certainly running jobs

## Slide 17: New SAG expansion rules
Previously a state was created for every schedulable job
Now a state is created for every job and possible number of cores
Can stimulate state-space explosion

## Slide 18: New SAG expansion rules
Purge states by checking that
  cores available
  More cores not available
  Precedence constraints are respected
Exploring more states
  👍 Is safe, does not make analysis invalid
  👎 Slower and more pessimistic
Initial state empty

## Slide 19: New SAG merge rules
We have to merge
  Availability times
  Groups of cores
  Certainly running jobs
Extend the intervals
Break the groups into same size
Merged
Keep only jobs running in both states (intersect)
Sate A
Sate B

## Slide 20: Our analysis results
Randomly generated task sets
System processors: 8
System tasks: 20 rigid tasks
Execution time variation: 50%
SCHEDULABLE
UNKNOWN
This project (sufficient test)
State-of-the-art
(sufficient test)
This project (sufficient test)

## Slide 21: Our analysis results
Randomly generated task sets
System processors: 8
System tasks: 20 moldable tasks
Execution time variation: 50%

## Slide 22: Our analysis results
Randomly generated task sets
System processors: 4
System tasks: 4 moldable tasks
Execution time variation: 50%
System utilization: 70%

## Slide 23: Agenda
Gang schedulability analysis
New scheduling policy

## Slide 24: JLFP limitations with moldable gang
Limited-Preemptive Moldable Reservation Gang Scheduler
Non-work conserving scheduler
Reserve cores of higher-priority tasks and distribute the remaining ones among lower priority tasks
Scheduling:
Scheduling:
Scheduling:
Scheduling:
JLFP scheduler
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20

## Slide 25: Reservation-based gang scheduler
Reservation-based
Reserve cores of higher-priority tasks and distribute the remaining ones among lower priority tasks
Non-work conserving scheduler
Scheduling:
Scheduling:
Scheduling:
Scheduling:
ResG scheduler
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20
 | Priority | Cores | Deadline | Execution time
 | High | 2 |  | 10
 | Mid-high | 3 | 20 | 5
 | Mid-low | 1 |  | 20
 | Low | 1 |  | 20

## Slide 26: Results JLFP vs ResG in simulator
This work
Baseline (JLFP)
System utilization %
Schedulability %
64%
55%
33%
Evaluated in simulator
Randomly generated task sets

## Slide 27: Summary
We proposed a new analysis for limited-preemptive moldable gang tasks
We showed the impact of choosing the level of parallelism in moldable gang tasks
We proposed a new non-work-conserving scheduling policy

## Slide 28: Conclusions
The maximum parallelism of a gang task has a big role in the schedulability
With a better scheduling policy one can improve the schedulability of moldable gang tasks

## Slide 29: Next steps
Further reduce sources of pessimism with precedence constraints
Provide an SAG analysis for the new scheduling policy
Notes: CLUSTER:
Higher confidence in the results
Test more parameters
Evaluate more systems

## Slide 30: Questions?

## Slide 31: How does SAG work?
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
Notes: Example of graph exploration:
If goes first no deadline miss
If goes first then has a deadline miss later
Example of graph exploration:
If 𝐽_1 goes first no deadline miss
If 𝐽_2 goes first then 𝐽_1 has a deadline miss later

## Slide 32: SAG analysis changes for gang
Check if execution with cores is possible
cores available
cores not available

## Slide 33: Colours
Primary
Boxes
Emphasis
Borders
Notes: SAG is the bridge between tests and simulations
Accurate and relatively fast
Explore space of possible schedules
Model scheduler decisions