## Slide 1: Scheduling Analysis of Limited-Preemptive Moldable Gang Tasks
20th of May, 2020
Geoffrey Nelissen
Mitra Nasri
Joan Marcè i Igual
Daily Supervisor
Co-supervisor

## Slide 2: Scheduling analysis state of the art
Closed-form analyses
Fast
Pessimist
Hard to extend
Accurate
Easy to extend
Not scalable
Exact tests in generic formal verification tools
Response analysis using schedule abstraction[1]
Accurate
Relatively fast
[1] Nasri et al., 2018
Industrial use cases are typically large, complex and require accurate analysis
Notes: SAG is the bridge between tests and simulations
Accurate and relatively fast
Explore space of possible schedules
Model scheduler decisions

## Slide 3: Schedule abstraction graph
It is a technique that allows:
  Search for all possible schedules
  Aggregate “similar” schedules
Every edge is a different scheduler decision
Every node is a different system state

## Slide 4: What is gang?
Parallel threads executed together as a “gang”
Execution does not start until there are enough free cores
Global scheduling
Gang Scheduling
Notes: Multiple related threads
Execute them together as a “gang”
Form a single job

## Slide 5: Why gang?
Efficient synchronization
Global scheduling
Gang Scheduling
Notes: Gang looks worse but it actually has advantages:
Global scheduling would be pre-empted when waiting for synchronization
Gang scheduling would busy wait and for the reply

## Slide 6: Why gang?
Efficient synchronization
Avoids overhead when loading initial data
Shows its full potential when executed non-preemptively
Global scheduling
Gang Scheduling
Notes: Global scheduling would load the same data multiple times
Gang scheduling would load the data once for all the jobs
This is more evident in non-preemptive execution

## Slide 7: Types of gang
Rigid: number of cores set by programmer
Notes: Three types:
Rigid gang: Number of cores fixed by programmer
Moldable gang: Number of cores between minimum and maximum. Scheduler chooses at scheduling time.
Malleable gang: Number of cores between minimum and maximum. Can vary during runtime

## Slide 8: Types of gang
Rigid: number of cores set by programmer
Moldable: number of cores assigned during scheduling
Notes: Three types:
Rigid gang: Number of cores fixed by programmer
Moldable gang: Number of cores between minimum and maximum. Scheduler chooses at scheduling time.
Malleable gang: Number of cores between minimum and maximum. Can vary during runtime

## Slide 9: Types of gang
Rigid: number of cores set by programmer
Moldable: number of cores assigned during scheduling
Malleable: number of cores can change during runtime
Notes: Three types:
Rigid gang: Number of cores fixed by programmer
Moldable gang: Number of cores between minimum and maximum. Scheduler chooses at scheduling time.
Malleable gang: Number of cores between minimum and maximum. Can vary during runtime

## Slide 10: Previous work
Introduced in the context of high-performance computing[1]
In real-time:
  We know that JLFP scheduler is not predictable/sustainable[2]
  Most of the work is focused in fully-preemptive solutions:
    Optimal scheduler for rigid gang (DP-Fair)[3]
    Moldable scheduler[4]
  Bundled scheduling[5]
    Tasks with precedence constraints modelled as a succession of bundles
    Our limited-preemptive definition comes from here
[1]Ousterhout, 1982
[2]Goossens et al., 2010
[3]Goossens et al., 2016
[4]Berten et al., 2011
[4]Wasly et al., 2017
Notes: Introduced in high-performance computing
Real-time:
  Fixed-priority is not predictable
  Fully-preemptive solutions:
    Optimal scheduler for rigid gang but high number of preemptions
    Moldable scheduler using moldable property to match deadlines
  Bundled scheduling:
    Precedence constraints modelled as a succession of bundles
    LP definition comes from here

## Slide 11: Summarizing
Notes: Example, three bundles.

## Slide 12: Summarizing
Rigid gang reserves the whole block
Bundled creates multiple rigid blocks with dependencies
Limited-Preemptive tries to schedule these blocks in a moldable way
Rigid gang scheduling
Bundled model scheduling
Limited-Preemptive scheduling
Notes: Rigid gang reserves a whole block for the three bundles
Bundled scheduling creates three individual rigid bundles
Limited-Preemptive creates three individual moldable bundles

## Slide 13: Our work

## Slide 14: Project goals
Design an accurate schedulability analysis for limited-preemptive moldable gang tasks with schedule abstraction graph
Propose a new scheduling algorithm to improve the schedulability of limited-preemptive moldable gang tasks

## Slide 15: SAG for gang tasks
Adaptation of JLFP for gang tasks
Changes required in SAG to model gang tasks
Testing method
  Generate tasks
  Execute them without any variation and expect the same results as the simulator
Issues identified
  The definition of certainly running jobs was not strict enough
  Precedence constraints is too pessimistic
  The first implementation of gang scheduling was too pessimistic. It is now fixed

## Slide 16: Adaptation of JLFP scheduler for gang tasks
Based on Global JLFP scheduler
  Work conserving scheduler
  Job with highest priority goes first
  All the predecessors of a job must have finished before it can start
Assigns maximum number of available cores to a job between the range of cores that the job allows
Notes: Explain what variations does JLFP have with gang scheduling

## Slide 17: SAG analysis changes for gang
Previously a state was created for every schedulable job
Now a state is created for every job and possible number of cores

## Slide 18: SAG evaluation
Generate gang task sets
Make sure that they are schedulable without any variation by using a simulator
Compare results with SAG results
  Without variation they should match exactly
  Used for testing of proper implementation
Generate results with execution time variation and/or release jitter

## Slide 19: Primary results
Either
  Gang is not what we expected
  There are issues in the analysis
We can do better

## Slide 20: Issues identified
State explosions
  Precedence constraints were ignored (bug in code)
  The new generated state was not entirely correct
Sources of pessimism
  Precedence constraints of higher priority jobs were ignored
  The analysis was not using the fact that multiple cores may be released at once
Fixed

## Slide 21: Pessimism in precedence constraints

## Slide 22: Pessimism in precedence constraints
is ready
has a successor with higher priority than
should never be able to start after finishes as the successor would start right away
Expected
Actual

## Slide 23: Pessimism in cores released
TODO: Change this image for the new one

## Slide 24: Pessimism in cores released
The analysis does not make difference between:
  Multiple jobs finishing
  One job finishing with multiple cores
The new job considers all the cores as individual jobs
Does not make the analysis invalid, just more pessimistic
Solving this makes the analysis faster

## Slide 25: Pessimism in cores released

## Slide 26: New scheduler

## Slide 27: New Scheduler
Limited-Preemptive Moldable Reservation Gang Scheduler
Non-work conserving scheduler
Reserve cores of higher-priority tasks and distribute the remaining ones among lower priority tasks
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
Scheduling:
Scheduling:
Scheduling:
Scheduling:
JLFP scheduler
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20

## Slide 28: New Scheduler
Limited-Preemptive Moldable Reservation Gang Scheduler
Non-work conserving scheduler
Reserve cores of higher-priority tasks and distribute the remaining ones among lower priority tasks
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
Scheduling:
Scheduling:
Scheduling:
Scheduling:
LPMRGS scheduler
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20

## Slide 29: Testing new scheduler
Tested on simulator
We want to test it now with schedule abstraction graph to see if it performs better than JLFP under execution variation possibilities

## Slide 30: Results JLFP vs new scheduler
Insert plot here comparing the two

## Slide 31: Conclusions
Gang scheduling is an interesting problem with a lot that can be done
It is possible to define an analysis with SAG for gang
  The analysis is too pessimistic
  The issues have been identified, a fix is on the way
Gang moldable properties have potential yet to be unlocked
Questions?

## Slide 32: Scheduling Analysis
Scheduling tests
  Pessimist
  Fast
  Exact
  Slow
Simulations
Schedule Abstraction
Graph[1]
  Accurate
  Relatively fast
[1] Nasri et al., 2018
Explore space of possible schedules for a given job set
Models scheduler decisions
Notes: SAG is the bridge between tests and simulations
Accurate and relatively fast
Explore space of possible schedules
Model scheduler decisions

## Slide 33: How does SAG work?
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
Notes: Example of graph exploration:
If goes first no deadline miss
If goes first then has a deadline miss later
Example of graph exploration:
If 𝐽_1 goes first no deadline miss
If 𝐽_2 goes first then 𝐽_1 has a deadline miss later

## Slide 34: Results method
Generate random task set
  Minimum and maximum number of cores fixed
  Total task cost is divided by number of cores
  10 segments per task
Make sure that the task set can be executed non-pre-emptively with JLFP and no jitter or execution time variation
Test task set with SAG
Generate 100 task sets per data point for:
  Utilization 10% to 90%
  Moldability from 0 to 7
  Total cores = 8

## Slide 35: Why these results?
There is pessimism in the SAG definition for:
  Precedence constraints
  Gang scheduling
We can solve it

## Slide 36: Difficulties related to SAG
We have to consider all scenarios.
The scheduler has to decide:
  When to release a job
  How many cores to assign to this job