## Slide 1: Scheduling analysis of limited-preemptive moldable gang tasks
3rd of June, 2020
Geoffrey Nelissen
Mitra Nasri
Joan Marcè i Igual
Daily Supervisor
Co-supervisor

## Slide 2: Real-time systems
Systems of which correctness does depends not only on logical results but also on timing constraints
Multicore systems

## Slide 3: Definitions
Task
  A functionality of the system
Job
  Instance of a task
Schedule
  A particular assignment of tasks to the processors and time intervals

## Slide 4: What is gang?
Parallel threads executed together as a “gang”
Execution does not start until there are enough free cores
Global scheduling
Gang Scheduling
Thread 4 starts after threads 0, 1, 2, and 3 finish
Related threads
Notes: Multiple related threads
Execute them together as a “gang”
Form a single job

## Slide 5: Why gang?
Efficient synchronization
Avoids overhead when loading initial data
Shows its full potential when executed non-preemptively
Global scheduling
Gang Scheduling
Notes: Global scheduling would load the same data multiple times
Gang scheduling would load the data once for all the jobs
This is more evident in non-preemptive execution

## Slide 6: Types of gang
Rigid: number of cores set by programmer
Moldable: number of cores assigned when job is dispatched
Malleable: number of cores can change during runtime
Notes: Three types:
Rigid gang: Number of cores fixed by programmer
Moldable gang: Number of cores between minimum and maximum. Scheduler chooses at scheduling time.
Malleable gang: Number of cores between minimum and maximum. Can vary during runtime
We choose moldable because:
Rigid can incur in loss of performance if not all cores are actually used
Malleable is hard to implement in reality

## Slide 7: Bundled scheduling vs Limited-Preemptive
Notes: Example, three bundles.

## Slide 8: Bundled scheduling vs Limited-Preemptive
Rigid gang reserves the whole block
Bundled creates rigid blocks with dependencies
Limited-Preemptive creates moldable blocks with dependencies
Rigid gang scheduling
Bundled model scheduling
Limited-Preemptive scheduling
Notes: Rigid gang reserves a whole block for the three bundles
Bundled scheduling creates three individual rigid bundles
Limited-Preemptive creates three individual moldable bundles

## Slide 9: How does JLFP work with gang?
Based on Global JLFP scheduler
Assigns maximum number of available cores to a job between the range of cores that the job allows
 | 2 | 3 | 100 | 15, 10
 | 2 | 2 | 20 | 15
 | 2 | 3 | 100 | 15, 10
 | 2 | 2 | 20 | 15
 | 2 | 3 | 100 | 15, 10
 | 2 | 2 | 20 | 15
 | 2 | 3 | 100 | 15, 10
 | 2 | 2 | 20 | 15
 | 2 | 3 | 100 | 15, 10
 | 2 | 2 | 20 | 15
 | 2 | 3 | 100 | 15, 10
 | 2 | 2 | 20 | 15
Scheduling:
Scheduling:
JLFP scheduler

## Slide 10: Previous work
[1]Ousterhout, 1982
[4]Goossens et al., 2010
[2]Goossens et al., 2016
[3]Berten et al., 2011
[6]Wasly et al., 2017
Introduced in HPC[1]
Preemptive solutions
Optimal rigid scheduler
(DP-Fair)[2]
Moldable scheduler[3]
Scheduling tests for JLFP[4] and EDF[5]
[5]Kato et al., 2009
Bundled scheduling[6]
Gang tasks with precedence constraints
Non-preemptive
Notes: Introduced in high-performance computing
Real-time:
  Fixed-priority is not predictable
  Fully-preemptive solutions:
    Optimal scheduler for rigid gang but high number of preemptions
    Moldable scheduler using moldable property to match deadlines
  Bundled scheduling:
    Precedence constraints modelled as a succession of bundles
    LP definition comes from here
What are the problems that we want to solve?
  Gang scheduling works best in non-preemptive solutions but no-one else has worked on that
  Rigid and moldable models have overhead when using precedence constraints
  There are no good moldable schedulers

## Slide 11: Our work

## Slide 12: Project goals
Design an accurate schedulability analysis for limited-preemptive moldable gang tasks
Propose a new scheduling algorithm to improve the schedulability of limited-preemptive moldable gang tasks

## Slide 13: Schedule abstraction graph
It is a technique that allows:
  Search for all possible schedules
  Aggregate “similar” schedules
Every edge is a different scheduler decision
Every node is a different system state

## Slide 14: SAG analysis changes for gang
Previously a state was created for every schedulable job
Now a state is created for every job and possible number of cores
Can lead to state-space explosion

## Slide 15: SAG analysis changes for gang
Adapt formulation to notion of multiple cores
Checks needed for
  cores available
  cores not available
  Precedence constraints with multiple cores
Defer state-space explosions
Earliest Start Time
Latest Start Time
Proofs

## Slide 16: Primary results
Either
  Gang is not what we expected
  There are issues in the analysis
We can do better
No EV
With EV

## Slide 17: Issues identified
State explosions
  Some precedence constraints were ignored
  New generated state was not entirely correct
Sources of pessimism
  Precedence constraints of higher priority jobs
  Multiple cores may be released at once
Fixed

## Slide 18: Pessimism in cores released
Before fix
After fix

## Slide 19: New scheduler

## Slide 20: JLFP limitations with moldable gang
Limited-Preemptive Moldable Reservation Gang Scheduler
Non-work conserving scheduler
Reserve cores of higher-priority tasks and distribute the remaining ones among lower priority tasks
Scheduling:
Scheduling:
Scheduling:
Scheduling:
JLFP scheduler
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20

## Slide 21: New Scheduler
Reservation-based
Reserve cores of higher-priority tasks and distribute the remaining ones among lower priority tasks
Non-work conserving scheduler
Scheduling:
Scheduling:
Scheduling:
Scheduling:
LPMRGS scheduler
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20
 | 2 | 2 | 100 | 10
 | 3 | 3 | 20 | 5
 | 1 | 1 | 100 | 20
 | 1 | 3 | 100 | 24, 13, 20

## Slide 22: Results JLFP vs new scheduler
This work

## Slide 23: Conclusions
Non-preemptive gang solves common multithreading issues
An analysis for non-preemptive can be defined
  It is still too pessimistic
The issues have been identified and a fix is on the way
Gang moldable properties have potential yet to be unlocked

## Slide 24: Questions?

## Slide 25: SAG analysis changes for gang
Check if execution with cores is possible
cores available
cores not available

## Slide 26: How does SAG work?
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 100 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
 | 10 | 15 | 10 | 30 | 1
 | 5 | 5 | 0 | 00 | 2
Notes: Example of graph exploration:
If goes first no deadline miss
If goes first then has a deadline miss later
Example of graph exploration:
If 𝐽_1 goes first no deadline miss
If 𝐽_2 goes first then 𝐽_1 has a deadline miss later

## Slide 27: Why gang?
Efficient synchronization
Global scheduling
Gang Scheduling
Notes: Gang looks worse but it actually has advantages:
Global scheduling would be pre-empted when waiting for synchronization
Gang scheduling would busy wait and for the reply
Example
Parallel SAT solvers use multiple threads that synchronize regularly to share learned clauses

## Slide 28: Scheduling analysis state of the art
Closed-form analyses
Fast
Pessimist
Hard to extend
Accurate
Easy to extend
Not scalable
Exact tests in generic formal verification tools
Response-time analysis using schedule abstraction[1]
Accurate
Relatively fast
[1] Nasri et al., 2018
Industrial use cases are typically large, complex and require accurate analysis
Notes: SAG is the bridge between tests and simulations
Accurate and relatively fast
Explore space of possible schedules
Model scheduler decisions

## Slide 29: SAG for gang tasks
Adapt JLFP to gang
Model gang in SAG
Code new model
Analyse results
Identify issues
Finish
Test in simulator
Test in SAG
Bugs
Pessimism

## Slide 30: How does JLFP work with gang?
Based on Global JLFP scheduler
  Work conserving scheduler
  Job with highest priority goes first
  All the predecessors of a job must have finished before it can start
Assigns maximum number of available cores to a job between the range of cores that the job allows
Notes: Explain what variations does JLFP have with gang scheduling

## Slide 31: SAG evaluation
Generate gang task sets
Make sure that they are schedulable without any variation by using a simulator
Compare results with SAG results
  Without variation they should match exactly
  Used for testing of proper implementation
Generate results with execution time variation and/or release jitter

## Slide 32: Colours
Primary
Boxes
Emphasis
Borders
Notes: SAG is the bridge between tests and simulations
Accurate and relatively fast
Explore space of possible schedules
Model scheduler decisions

## Slide 33: Scheduling Analysis
Scheduling tests
  Pessimist
  Fast
  Exact
  Slow
Simulations
Schedule Abstraction
Graph[1]
  Accurate
  Relatively fast
[1] Nasri et al., 2018
Explore space of possible schedules for a given job set
Models scheduler decisions
Notes: SAG is the bridge between tests and simulations
Accurate and relatively fast
Explore space of possible schedules
Model scheduler decisions

## Slide 34: Results method
Generate random task set
  Minimum and maximum number of cores fixed
  Total task cost is divided by number of cores
  10 segments per task
Make sure that the task set can be executed non-pre-emptively with JLFP and no jitter or execution time variation
Test task set with SAG
Generate 100 task sets per data point for:
  Utilization 10% to 90%
  Moldability from 0 to 7
  Total cores = 8

## Slide 35: Why these results?
There is pessimism in the SAG definition for:
  Precedence constraints
  Gang scheduling
We can solve it

## Slide 36: Difficulties related to SAG
We have to consider all scenarios.
The scheduler has to decide:
  When to release a job
  How many cores to assign to this job

## Slide 37: SAG for gang tasks
Adaptation of JLFP for gang tasks
Changes required in SAG to model gang tasks
Testing method
  Generate tasks
  Execute them without any variation and expect the same results as the simulator
Issues identified
  The definition of certainly running jobs was not strict enough
  Precedence constraints is too pessimistic
  The first implementation of gang scheduling was too pessimistic. It is now fixed

## Slide 38: Pessimism in precedence constraints

## Slide 39: Pessimism in precedence constraints
is ready
has a successor with higher priority than
should never be able to start after finishes as the successor would start right away
Expected
Actual

## Slide 40: Pessimism in cores released
TODO: Change this image for the new one

## Slide 41: Pessimism in cores released
The analysis does not make difference between:
  Multiple jobs finishing
  One job finishing with multiple cores
The new job considers all the cores as individual jobs
Does not make the analysis invalid, just more pessimistic
Solving this makes the analysis faster

## Slide 42: Testing new scheduler
Tested on simulator
We want to test it now with schedule abstraction graph to see if it performs better than JLFP under execution variation possibilities